## Slide 1: AI Water Quality Forecasting System
CSE276: Artificial Intelligence Foundations | CA1 Project P18 | Team ZJ18
Prince Sahu
Reg. No. 12508888
Ridham Dadwal
Reg. No. 12514189
Lovely Professional University

## Slide 2: Introduction
Why water quality matters
Rivers carry pollution from cities, farms and industry, and their quality changes with season and rainfall.
Why forecast it
Monitoring shows today's quality. A forecast gives authorities time to treat water, warn users and plan.
What this project does
Computes a Water Quality Index, forecasts it with AI models and shows alerts in a demo app.

## Slide 3: Forecasting river water quality for early action
Problem (SIH1694)
Authorities need to know what river water quality will be soon, not only what it is today. We build a multivariate forecasting and decision-support system on public data.
Objectives
Clean multivariate water-quality data
Compute a Water Quality Index (WQI)
Forecast WQI and beat a naive baseline
Turn forecasts into alerts in a demo app

## Slide 4: System overview
Part A (real, yearly) and Part B (synthetic, daily) share one decision-support app.

## Slide 5: Part A data: real Indian river stations
1,988
rows (station-years)
439
stations
20
states and UTs
2003-14
yearly averages
Source: Kaggle "Indian water quality data" (Anbarivan.N.L), government-sourced
Parameters: temperature, DO, pH, conductivity, BOD, nitrate, fecal and total coliform
Not available: turbidity, daily or monthly readings

## Slide 6: Part B data: synthetic daily series
2,192
days, 2019 to 2024
6
parameters
3%
missing per column
15
bad readings added
Why: no public daily river dataset found for this assignment
Design: annual temperature cycle, monsoon rise in turbidity and BOD, fall in conductivity and pH
Smooth by design, so scores are optimistic and used only to validate the 7-day pipeline

## Slide 7: Cleaning the real data
Missing values
Text "NAN" became missing and was never replaced by zero
Station identity
About 6% of codes were "NAN"; location name used instead, rows with neither dropped
State field
203 raw values became 20 states and UTs; location text split out, spellings unified
Short histories
Average 4.5 years per station; at least a quarter have only one year

## Slide 8: Water Quality Index (WQI)
Part A: 0 to 100, higher is better
Banded sub-scores, weights: DO 0.281, coliform 0.281, BOD 0.234, pH 0.165
Excellent 90+, Good 70-90, Medium 50-70, Bad 25-50, Very Bad below 25
1,955 station-years: Good 1,434, Excellent 219, Medium 195, Bad 93, Very Bad 14
Part B: higher is worse
Weighted arithmetic index from pH, DO, turbidity, conductivity and BOD
Excellent up to 50, Good to 100, Poor to 200, Very Poor to 300, Unsafe above
Mean 94.7; Good 1,508 days, Poor 684 days

## Slide 9: Forecasting setup
Part A: next year
Readings and WQI in year t predict WQI in year t+1
Time split: train 2003-2011 (898 pairs), test 2012-2013 (478 pairs)
Naive, Linear, Random Forest, XGBoost, plus delta versions that predict the change
Part B: 7 days
Lags (0 to 14 days), 7-day rolling mean and seasonal terms
Time split: first 80% train, last 20% test (63 forecasts)
Naive, SARIMAX, Random Forest, XGBoost
Metrics: MAE, RMSE, R2 or MAPE, and category accuracy. No random splits.

## Slide 10: Real data: modest gain over the naive baseline
Best model: Linear (delta), RMSE 5.72 and R2 0.844, about 7% below naive (6.16). Naive keeps the best MAE (3.75) and category accuracy (83.89%).

## Slide 11: Real data: WQI categories and delta learning
Predicting the change cut RMSE from 6.65 to 5.94 for Random Forest and from 7.08 to 6.19 for XGBoost.

## Slide 12: Synthetic data: the 7-day pipeline works
Model | MAE | RMSE | MAPE (%) | Category accuracy (%)
XGBoost | 3.75 | 4.85 | 4.32 | 96.83
Random Forest | 3.93 | 5.13 | 4.51 | 98.41
SARIMAX | 5.00 | 6.11 | 5.56 | 96.83
Naive | 5.52 | 6.55 | 6.15 | 96.83
XGBoost RMSE is about 26% lower than naive. The series is smooth by design, so these scores are optimistic.

## Slide 13: Decision-support app (Streamlit)
Real data tab
Readings, model comparison and the yearly trend for the chosen station
Synthetic tab
7-day forecast with status alert: acceptable, caution or alert

## Slide 14: Conclusion and limits
What we found
Simple models predicting WQI change slightly beat the naive baseline on real yearly data. Year-to-year water quality is hard to beat with last year's value.
Limits and next steps
Yearly averages, short station histories, no significance test. Next: real daily or monthly data and live sensor feeds.
Code: https://github.com/princesahu500000-cpu/ai-water-quality-forecasting
Data: Kaggle Indian water quality data (Anbarivan.N.L). Criteria: CPCB Water Quality Criteria.